Hikvision video intercom SIP function Introduction

（2019-6-6）

Product involved:

| Device Model | Firmware |
| --- | --- |
| DS-KH8350-WTE1 | V2.0.21_build190314 |
| DS-KH8350-TE1 | V2.0.21_build190314 |
| DS-KH6320-WTE1 | V2.0.21_build190314 |
| DS-KH6320-TE1 | V2.0.21_build190314 |
| DS-KH8520-WTE1 | V2.0.21_build190314 |
| DS-KD8102-V | V1.5.1_ build 190130 |
| DS-KD8002-VM | V1.5.1_ build 190130 |

Note:

- Because standard SIP services involve public network holes, signaling forwarding, and diverse audio and video formats. The current use of Hikvision standard SIP is limited.

- If you have any questions about SIP, please complete this excel sheet and contact Hikvision's technical support.

- In the public network environment, the video transmission of the device is bound to be limited by many factors. It will cause poor picture quality, inability to display pictures, and so on.

Table of Contents

How to configure device's SIP service through the client	2

How to configure indoor station’s SIP service through local interface	4

Comparison of private protocol and standard SIP protocol	7

How to set the SIP phone and how to use the SIP phone to open the door	8

List of supported SIP phone	14

How to configure device's SIP service through the client

1. Add the device to the Client.

2. Enter the remote configuration  Intercom  Intercom Protocol, and change the protocol to ‘SIP protocol’, then waiting the device reboot.

3. Enter the remote configuration  Network  SIP settings, check the data which you set in your SIP server, then fill the corresponding column.

- By default

- SIP server example and finished condition

- Confirm that the device has been registered

How to configure indoor station’s SIP service through local interface

- Enter the Settings interface

- Select ‘More’ interface then click the Configuration

Then enter the admin password which is 888999.

- Enter ‘SIP Settings’ interface and click the SIP Protocol Settings

Select Standard Protocol

Then let the device reboot

Waiting the device reboot

- The SIP Settings interface will changed like this picture

Click the VOIP Account Setting to set the SIP account.

- The interface is shown below

SIP server example and finished condition

Click ‘OK’ to save the settings.

- Go back to the main interface to make sure the settings is complex

Comparison of private protocol and standard SIP protocol

| Indoor station |  |  |
| --- | --- | --- |
|  | Private Protocol | SIP Protocol |
| HikConnect APP | √ | × |
| Indoor extension | √ | × |
| Live view | √ | × |
| Call to the door station | √ | × |
| Private password | √ | × |
| Automatic capture picture | √ | × |
| Door station |  |  |
|  | Private Protocol | SIP Protocol |
| Sub-door station | √ | × |
| Doorphone Mode | √ | × |
| Outer door station | √ | × |
| Public password | √ | √ |

How to set the SIP phone and how to use the SIP phone to open the door

Note: Test example product is GXV3275 of Grand Stream

Firmware: 1.0.1.54

- Configuring the GXV3275 Using Web Browser

The default username and password for administrator are “admin” and “admin”;

The default username and password for user are “user” and “123”.

Click the Account  Account1 (all off Account 1 to 6 is ok) to set the SIP account.

The interface is shown below

SIP server example and finished condition

Click the Save icon and select ‘Apply’

Then go back to the status interface to confirm that the device is registered to the sip server

- Configuring the GXV3275 by local interface

Click the Settings to enter settings interface

Click Account to enter the SIP account interface

We only use the Account1 (all off Account 1 to 6 is ok), so enter the account1 interface

SIP server example and finished condition

Go back to the main interface, we can check we are already connect the SIP phone to the SIP server.

c. Test to use the door station to call the SIP phone

Click the Video Answer to answer the call

And you can choose to use the keypad, press key ‘#’ to open the door

List of supported SIP servers

Brekeke 3.7.7.3

List of supported SIP phone

GrandStream GXV3275

Yealink SIP-T46G

First Choice for Security Professionals

HIKVISION Technical Support